## Slide 1: L5 – Memory System

## Slide 2: Memory Performance
Memory Wall [McKee’94]
  CPU-Memory speed disparity
  100’s of cycles for off-chip access
DRAM
(2X/10 yrs)
Processor-Memory
Performance Gap: (grows 50% / year)
Proessor (2X/1.5yr)
Performance
Year
Moore’s Law

## Slide 3: Memory Hierarchy
CPU
MMU
L1
I-Cache
L1
D-Cache
L2 Unified Cache
Memory

## Slide 4: Memory Hierarchy in Multicore
L2-Cache
C0
C1
L1$
L1$
C2
C3
L1$
L1$
Memory Controller
Memory
1 – 2 Cycles
100 – 300 cycles
10 – 15 cycles

## Slide 5: Memory Performance
Memory Wall [McKee’94]
  CPU-Memory speed disparity
  100’s of cycles for off-chip access
Bandwidth Wall [ISCA’09]
  More cores and limited off-chip bandwidth
  Cores double every 18 months
  Pincount grows only by 10%
Off-chip accesses are expensive !
Memory System Performance is Critical

## Slide 6
Core 0
Core 1
Core 15
...
L1D
L1I
L1D
L1I
L1D
L1I
L2 Cache
(Off Chip)
Main
Memory
Hit
Memory
Controller
Miss
Multi-Core Processor
L3 Cache
(LLSC)
L2 Cache
Core 14
L1D
L1I
Memory Hierarchy in Multicore

## Slide 7: Memory Bank Organization

## Slide 8: SRAM vs. DRAM
SRAM is preferable for register files and L1/L2 caches
  Fast access
  No refreshes
  Simpler manufacturing (compatible with logic process)
  Lower density (6 transistors per cell)
  Higher cost
DRAM is preferable for stand-alone memory chips
  Much higher capacity
  Higher density
  Lower cost
Reading: S. Rixner, et. al, “Memory Access Scheduling”, ISCA 2000

## Slide 9: Memory subsystem organization
Memory subsystem organization
  Channel
  DIMM
  Rank
  Chip
  Bank
  Row/Column

## Slide 10: Memory subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
“Channel”
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM MEMORY CONTROLLER

## Slide 11: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 12: Rank
Rank 0 (Front)
Rank 1 (Back)
Data <0:63>
CS <0:1>
Addr/Cmd
<0:63>
<0:63>
Memory channel

## Slide 13: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 14: Breaking down a Chip
Chip 0
<0:7>
8 banks
Bank 0
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 15: Breaking down a Bank
Bank 0
<0:7>
row 0
row 16k-1
...
2kB
1B
1B (column)
1B
Row-buffer
1B
...
<0:7>

## Slide 16: Memory subsystem organization
Memory subsystem organization
  Channel
  DIMM
  Rank
  Chip
  Bank
  Row/Column
Ch
Rk
D
Row
Bank
Col
Address:
Dev.

## Slide 17: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Channel 0
DIMM 0
Rank 0
Mapped to

## Slide 18: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 19: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 20: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 21: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
A 64B cache block takes 8 I/O cycles to transfer.
During the process, 8 columns are read sequentially.
. . .

## Slide 22: Overview of a DRAM based memory
Memory Controller
Data Read (or Write) operations
Control
Address
Data
Rows
Columns
Bank
Logic
Row Buffer
DRAM Bank
DIMM
Rank
Device
Bank
Notes: Need to say that the over all structure remains the same whether it is DRAM or PCM or any other technology

## Slide 23: Page Mode DRAM
A DRAM bank is a 2D array of cells: rows x columns
A “DRAM row” is also called a “DRAM page”
“Sense amplifiers” also called “row buffer”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for activate command

## Slide 24: DRAM Bank Operation
Row Buffer
Access Address
(Row 0, Column 0)
Row decoder
Column decoder
Row address 0
Column address 0
Data
Row 0
Empty
Access Address
(Row 0, Column 1)
Column address 1
Access Address
(Row 0, Column 9)
Column address 9
Access Address
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Slide Source: Onur Mutlu, CMU

## Slide 25: Basic DRAM Operations
ACTIVATE  Bring data from DRAM core into the row-buffer
READ/WRITE  Perform read/write operations on the contents in the row-buffer
PRECHARGE  Store data back to DRAM core (ACTIVATE discharges capacitors), put cells back at neutral voltage
H
M
Memory Requests
PRE
RD
ACT
M
RD
Row buffer hits are faster and
consume less power
PRE
RD
ACT
Notes: Once again need to say that the operations are same for other technologies too

## Slide 26: Latency Components in DRAM Operation
Timing Constraints – DDR3 (1066)

## Slide 27: Latency Components: Basic DRAM Operation
CPU → controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
Controller → DRAM transfer time
DRAM bank latency
  Only Rd/Wr if row is “open” OR
  Act + Rd/Wr if array is precharged OR
  Pre + Act + Rd/Wr (worst case)
Data Burst time
  Read multiple consecutive columns (4/8/16) in succession
DRAM → CPU transfer time (through controller)

## Slide 28: Multiple Banks (Interleaving) and Channels
Multiple banks
  Enable concurrent DRAM accesses
  Bits in address determine which bank an address resides in

## Slide 29: How Multiple Banks/Channels Help

## Slide 30: Address Mapping (Single Channel)
Single-channel system with 8-byte memory bus
  2GB memory, 8 banks, 16K rows & 2K columns per bank
Row interleaving
  Consecutive rows of memory in consecutive banks
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)

## Slide 31: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
64B
Bank 0
Row 0
Col 0:7
. . .
Bank 0 Row 0
Col 8:15
64B

## Slide 32: Address Mapping (Single Channel)
Single-channel system with 8-byte memory bus
  2GB memory, 8 banks, 16K rows & 2K columns per bank
Row interleaving
  Consecutive rows of memory in consecutive banks
Cache block interleaving
    Consecutive cache block addresses in consecutive banks
    64 byte cache blocks
    Accesses to consecutive cache blocks can be serviced in parallel
    How about random accesses? Strided accesses?
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits

## Slide 33: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
64B
Bank 0
Row 0
Col 0:7
. . .
Bank 1
Row 0
Col 0:7
64B

## Slide 34: Multiple Banks (Interleaving) and Channels
Multiple banks
  Enable concurrent DRAM accesses
  Bits in address determine which bank an address resides in
Multiple independent channels serve the same purpose
  But they are even better because they have separate data buses
  Increased bus bandwidth
Enabling more concurrency requires reducing
  Bank conflicts
  Channel conflicts
How to select/randomize bank/channel indices in address?
  Lower order bits have more entropy
  Randomizing hash functions (XOR of different address bits)

## Slide 35: Interaction with VirtualPhysical Mapping
Operating System influences where an address maps to in DRAM
Operating system can control which bank a virtual page is mapped to. It can randomize Page<Bank,Channel> mappings
Application cannot know/determine which bank it is accessing
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 b)
Page offset (12 bits)
Physical Frame number (19 bits)
Page offset (12 bits)
Virtual Page number (36 bits)
VA
PA
PA

## Slide 36: DRAM Refresh
Capacitors leak and lose charge  Need periodic restoration of charge
JEDEC Spec: At normal temp, cell retention time limit is 64ms. At high (extended) temp, retention time halves to 32ms.
The memory controller issues refresh operations periodically.
Normal Access
Normal Access
Normal Access
Normal Access
Refresh
Normal Access
Assume 4GB DRAM with 2KB pages, organized as 16 banks
2M pages total, 128K pages per bank
Refreshing a page takes 20ns (ACTIVATE+PRECHARGE)
Refreshing all pages in a bank  2.56ms!
 2.56/64 = 4% overhead!
Normal Access
…
10 – 30 ns
2.56 ms

## Slide 37: DRAM Refresh (I)
Burst refresh: All rows refreshed immediately after one another
  -- Implications on performance?
  -- DRAM bank unavailable while being refreshed
  -- Long pause times: If we refresh all rows in burst, every 64ms the DRAM will be unavailable until refresh ends
Distributed refresh: Each row refreshed at a different time, at regular intervals

## Slide 38: DRAM Refresh (II)
Distributed refresh eliminates long pause times
How else we can reduce the effect of refresh on performance?
  Can we reduce the number of refreshes?

## Slide 39: DRAM Controller
Purpose and functions
  Ensure correct functioning of DRAM (refresh)
  Service DRAM requests while obeying timing constraints of DRAM chips
    Constraints: resource conflicts (bank, bus, channel), minimum write-to-read delays
    Translate requests to DRAM command sequences
  Buffer and schedule requests to improve performance
    Reordering and row-buffer management
  Manage power consumption and thermals in DRAM
    Turn on/off DRAM chips, manage power modes

## Slide 40: DRAM Memory Controller
Frontend
  Request/Response Buffers
  Memory mapping
  Arbiter
Controller Backend
  Command Generator
Timing to be obeyed
Notes: Once again need to say that the operations are same for other technologies too

## Slide 41: DRAM Parameters
Notes: Once again need to say that the operations are same for other technologies too

## Slide 42: DRAM Command Summary
Notes: Once again need to say that the operations are same for other technologies too

## Slide 43: Memory Access Scheduling: Motivation

## Slide 44: Memory State Diagram & Resource Usage

## Slide 45: Memory Access Scheduling
A row-conflict memory access takes significantly longer than a row-hit access
Current controllers take advantage of the row buffer
Commonly used scheduling policy (FR-FCFS) [Rixner, ISCA’00]
  (1) Row-hit (column) first: Service row-hit memory accesses first
  (2) Oldest-first: Then service older accesses first
This scheduling policy aims to maximize DRAM throughput
Slide Source: Onur Mutlu, CMU

## Slide 46: Memory Access Scheduler
Selects one or more operations (Precharge, Activate, or Column Access) each cycle

## Slide 48: FRFCFS Scheduling
Row Buffer
Row decoder
Column decoder
Data
Row 0
T0: Row 0
Row 0
T1: Row 16
T0: Row 0
T1: Row 111
T0: Row 0
T0: Row 0
T1: Row 5
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
Request Buffer
T0: streaming thread
T1: non-streaming thread
Slide Source: Onur Mutlu, CMU

## Slide 49: Benchmarks

## Slide 50
The 14% drop in sustained bandwidth from the unit load benchmark to the unit benchmark shows the performance degradation imposed by forcing intermixed load and store references to complete in order.
The unit conflict benchmark further shows the penalty of swapping back and forth between rows in the DRAM banks, which drops the sustainable bandwidth down to 51% of the peak.
The random benchmarks sustain about 15% of the bandwidth of the unit load benchmark.

## Slide 51
The Figure presents the sustained memory bandwidth for each
memory access scheduling algorithm on the given benchmarks.
These aggressive scheduling algorithms improve the
memory bandwidth of the microbenchmarks by 106-144%,
the applications by 27-30%, and the application traces by
85-93% over in-order scheduling.

## Slide 52: Things to Ponder
How about the cost of implementing the Memory Access Scheduler?
How about the extra logic and the power dissipation?
Why contemporary cache organizations waste memory bandwidth to reduce memory latency ?

## Slide 53: Major Trends Affecting Memory
Need for main memory capacity and bandwidth increasing
New need for handling inter-application interference; providing fairness, QoS
Main memory energy/power is a key system design concern
DRAM is not scaling well
New memory technologies becoming available!
  Non-volatile memory
  Stacked DRAM memory

## Slide 54: Emerging Memory Technology
Non-Volatile Memory technology
  Phase Change Memory (PCM), Magnetic RAM (MRAM), Resistive RAM (RRAM), Spin Torque Transfer RAM (STT-RAM), …
Slide Source: Moin Quereshi, Georgia Tech.

## Slide 55: Emerging Memory Technology
Phase Change Memory
  Data stored by changing phase of a special material
  Phase change material (chalcogenide glass) exists in two states:
    Amorphous: high resistivity – reset state or 0
    Crystalline: low resistivity – set state or 1
  Data read by detecting material’s resistance
  Non-volatality and low idle power (no refresh)
  Expected to scale (to 9nm), denser than DRAM, and can store multiple bits/cell
  Higher Write latency and write-energy
  Endurance issues (cell dies after 108 writes)
Slide Source: Onur Mutlu, CMU

## Slide 56: DRAM – PCM Hybrid Memory
PCM-based (main) memory be organized?
Hybrid PCM+DRAM
  How to partition/migrate data between PCM and DRAM
  Is DRAM a cache for PCM or part of main memory?
  How to design the hardware and software
Slide Source: Onur Mutlu, CMU

## Slide 57: PCM-based Main Memory
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings
Slide Source: Onur Mutlu, CMU

## Slide 58: Stacked DRAM
DRAM vertically stacked on the processor die.
Stacked DRAMs offer
  High bandwidth
  Large capacity
  Same or slightly lower latency.
3-D Stacked DRAM
2.5-D Stacked DRAM
Can be used as
Cache or
Part of Memory

## Slide 59: Processor Orgn. With DRAM Cache
Core 0
Core 1
Core N
.
.
.
L1D
L1I
L1D
L1I
L1D
L1I
L2
(LLSC)
(~8MB)
Stacked
DRAM
Cache
(~1GB)
(Off Chip)
Main
Memory
Hit
Memory
Controller
Miss
Processor with Stacked DRAM

## Slide 60: Problems in Architecting Large DRAM Caches
Small cache line size (64 B): Lower spatial locality, but reduced wasted bandwidth and cache capacity
  Problem: Large tag store of 10’s of MB
    E.g. 256MB DRAM cache needs ~20MB tag store
Large cache block size (2048B)
  Low tag store overhead – SRAM tag-store
  Problem: wasted off-chip bandwidth and wasted cache capacity
Option 1: SRAM Tags
Low Hit Time, but Impractical (Large SRAM)
[AlloyCache, ATCache]
Option 2: Tags in DRAM
Naïve design has 2x latency
(Two accesses -- tag and data)
[FootPrintCache, CHOP]

## Slide 61: Processor Orgn. With DRAM Cache
Core 0
Core 1
Core N
.
.
.
L1D
L1I
L1D
L1I
L1D
L1I
L2
(LLSC)
DRAM
Cache
(Vertically
Stacked)
(Off Chip)
Main
Memory
Tag-Pred
Hit
Memory
Controller
Miss
Processor with Stacked DRAM
MetaData on SRAM
MetaData on DRAM

## Slide 62: Research Issues in Multicore Memory Hierarchy
L2-Cache
C0
C1
L1$
L1$
C2
C3
L1$
L1$
Memory
Memory Controller
Scheduling of Memory Request
Memory Organization/ Technology
Cache Sharing across Multi-cores
DRAM Cache

## Slide 63: Architecture/System Trends
Sharing of memory hierarchy
More cores and components
  More pressure on the memory hierarchy
Different cores have different performance requirements
  Memory hierarchies do not distinguish between cores
Different goals for different systems/users
  System throughput, fairness, per-application performance
  Modern hierarchies are not flexible/configurable
Asymmetric cores: Performance asymmetry, CPU+GPUs, accelerators, …
Slide Source: Onur Mutlu, CMU