## Slide 1: L6 – Data Parallelism

## Slide 2: Different Types of Parallelism
Instruction-Level Parallelism
  VLIW, Superscalar, EPIC
Thread-Level Parallelism
  SMT, Multicore
Task-Level Parallelism
  Multicore Processors
  Multiprocessor Systems: Shared and Distributed Memory
Data-Level Parallelism

## Slide 3: Data Level Parallelism
Vector Processors
  Single instruction on multiple data (elements of a vector – temporal)
Array Processors
  Single instruction on multiple data (elements of a vector / array – spatial )
Modern Processors
  MMX / SSE / AVX instructions
Graphic Processing Units
  Multiple SIMD Cores in each Streaming Processors

## Slide 4: Intel SIMD Extensions
New SIMD instructions, new registers
Introduced in phases/groups of functionality
  MMX (1993 – 1999)
    64 bit width operations
  SSE – SSE4 (1999 –2006)
    128 bit width operations
  AVX, FMA, AVX2, AVX-512 (2008 – …)
    256 – 512 bit width operations
© RG@SERC,IISc

## Slide 5: SIMD Operations
SIMD execution
  performs operation in parallel on an array of 2, 4, 8,16 or 32 values
Operation ⊗ can be a
  data movement instruction
  arithmetic instruction
  logical instruction
  comparison instruction
  conversion instruction
  shuffle instruction
X0
X1
X2
X2
Y0
Y1
Y2
Y3
Z0
Z1
Z2
Z3
⊗
⊗
⊗
⊗

## Slide 6: Intel SIMD Registers (AVX-512)
ZMM0
YMM0
XMM0 – XMM15
  128-bit registers
  SSE
YMM0 – YMM15
  256-bit registers
  AVX, AVX2
ZMM0 – ZMM31
  512-bit registers
  AVX-512
XMM0
ZMM1
YMM1
XMM1
ZMM31
YMM31
XMM31
…
© RG@SERC,IISc

## Slide 7: SSE/AVX Data Types
Operation on 32 8-bit values in one instruction
Or 4 64-bit values, 8 32-bit values, or 16 16-bit values!
YMM0
float
float
float
float
double
double
int32
int32
int32
int32
float
float
float
float
double
double
int32
int32
int32
int32
16
16
8
8
16
16
8
8
8
8
8
8
16
16
8
8
16
16
8
8
8
8
8
8
16
16
8
8
16
16
8
8
8
8
8
8
16
16
8
8
16
16
8
8
8
8
8
8
255
0
© RG@SERC,IISc

## Slide 8: Exploiting Vector Instructions
Automatic vectorization by the compiler
  no explicit vectorized programming is needed
  arrange code so that compiler can detect vectorization
Explicit arithmetic expression on vector data types
  declare variables of a vector type and express computations as normal arithmetic on vector variables
  the compiler generates vector instructions
Use compiler intrinsic for vector operations
  functions implement vector instructions in high-level language
  requires detailed knowledge of the vector instructions

## Slide 9: Automatic Vectorization
In gcc, flags “-O3 –mavx –mavx2” attempts automatic vectorization
Works pretty well for simple loops
But not for anything complex
  E.g., naïve bubble sort code not parallelized at all
float X[256], Y[256], Z[256];
{ int i;
for (i=0; i<256; i++)
Z[i] = X[i] * Y[i];
}
L1: vmovdqa xmm1, X[rax]
vmovdqa xmm2, Y[rax]
vpmulld xmm0, xmm1, xmm2
vmovap Z[rax], xmm0
add rax, 16
cmp rax, 256
jne .L1
© RG@SERC,IISc

## Slide 10: Explicit Arithmetic Operations with Vector Data Type
Declare variables of vector data types and express computations with normal arithmetic expressions
  the arithmetic operations (+, –, *, etc.) are overloaded with the corresponding vector operations
Compiler generates vector instructions for the arithmetic operations
__m128 *x_ptr, *y_ptr, z_ptr ; /* Pointers to vectors */
x_ptr = (__m128 *) X; /* Set pointers to the data */ y_ptr = (__m128 *) Y;
z_ptr = (__m128 *) Z;
for (i=0; i<n/4; i++) {
z_ptr[i] = x_ptr[i] * y_ptr[i]; /* Do the computation */
}

## Slide 11: Vector Intrinsic Functions
Declare vector variables of the appropriate type
Load data values into the variables
Do arithmetic operations on the vector variables by calling intrinsic functions
float float *X, float *Y, float *Z ;
{ __m128 x_vec, y_vec, z_vec, res_vec; /* Vector variables */
for (i=0; i<n; i+=4) {
/* Vector of 4 alpha values */
x_vec = _mm_load_ps(&X[i]);
y_vec = _mm_load_ps(&Y[i]);
res_vec = _mm_mul_ps (x_vec, y_vec) ; /* Compute */ _mm_store_ps (&Z[i], res_vec); /* Store the result */
}
}

## Slide 12: Intel Xeon Phi (Many Integrated Cores)
16-wide SIMD engine
Gather / Scatter Unit
Vector Mask

## Slide 13: The Processor Core
Vector processing unit (VPU) associated with each core.
Sixteen-element wide SIMD engine
Gather / Scatter Unit
Vector Mask
13

## Slide 14: Generalization: Applicable to any data parallel workloads
Identical, Independent computation on multiple data inputs
3,7
4
2,7
5
1,7
6
0,7
7
Source: Arkaprava Basu, CSA, IISc

## Slide 15: A SIMT Approach
Single Instruction Multiple Thread
Split identical, independent work over multiple lockstep threads
Multiple Threads + Scalar Ops  One PC, Multiple register files
7
6
5
4
Fetch
Decode
Execute
Memory
Writeback
Execute
Execute
Execute
Memory
Memory
Memory
Writeback
Writeback
Writeback
Program
0,7
1,7
2,7
3,7
Source: Arkaprava Basu, CSA, IISc

## Slide 16: A SIMT Approach
Single Instruction Multiple Thread
Split identical, independent work over multiple lockstep threads
Multiple Threads + Scalar Ops  One PC, Multiple register files
7
6
5
4
Fetch
Decode
Execute
Memory
Writeback
Execute
Execute
Execute
Memory
Memory
Memory
Writeback
Writeback
Writeback
Program
0,7
1,7
2,7
3,7
Source: Arkaprava Basu, CSA, IISc
Single Instruction Multiple Thread (SIMT) execution model.
Many SIMT “threads” (lockstep execution) grouped together (warp) for execution
Many such warps scheduled together (in a Streaming Multiprocessor (SM)) and context-switched (multithreading) among themselves to hide stalls.
Multiple SM’s execute groups of warps in parallel.

## Slide 17: Graphic Processing
FIGURE A.2.3 Graphics logical pipeline. Programmable graphics shader stages are blue, and fixed-function blocks are white. Copyright © 2009 Elsevier, Inc. All rights reserved.
Graphics Logical Pipeline

## Slide 18: Unified GPU Architecture
FIGURE A.2.4 Logical pipeline mapped to physical processors. The programmable shader stages execute on the array of unified processors, and the logical graphics pipeline dataflow recirculates through the processors. Copyright © 2009 Elsevier, Inc. All rights reserved.

## Slide 19: Graphic Processor 8800

## Slide 20: Graphics Processing Unit (GPU)
Processor optimized for 2D/3D graphics, video, visual computing, and display.
Highly parallel, highly multithreaded multiprocessor optimized for visual computing.
Provides real-time visual interaction with computed objects via graphics images, and video.
Serves as both a programmable graphics processor and a scalable parallel computing platform.
Notes: Over the past few years . . .
. . . Allow the programmer to create 1000’s of threads each of which executes the same
Previous work has successfully ported over several applications to the GPU and in some cases

## Slide 21: Comparing CPU and GPU

## Slide 22: Comparing CPU and GPU
8-24 CPU cores @ 3 GHz
380 – 1200 GFLOPS
2880 CUDA cores @ 1.67 GHz
1500 – 7500 GFLOPS
GPU
CPU
PCI-e
Memory
C0
C1
C7
QPI
IMC
SLC
Memory
© RG@SERC,IISc

## Slide 23: Rise of GPGPU Computing
GPUs have become a popular platform for general purpose applications
Order of magnitude speedup over single-threaded CPU
New Programming Models
  CUDA
  OpenCL
  OpenACC
  OpenMP 4.x
Notes: Over the past few years . . .
. . . Allow the programmer to create 1000’s of threads each of which executes the same
Previous work has successfully ported over several applications to the GPU and in some cases

## Slide 24: Next Few slides from

## Slide 25: CUDA Programming

## Slide 26: CUDA Programming

## Slide 27: Processing Flow

## Slide 28: Processing Flow

## Slide 29: Processing Flow

## Slide 30
Execution of CUDA on GPUs
A CUDA kernel consists of an array of light-weight threads
  All threads run the same code, but on different data
  Each thread has an ID that it uses to compute memory addresses and make control decisions
7
6
5
4
3
2
1
0
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
threadID

## Slide 31: Threads, Warps, Thread Blocks
Group threads into multiple blocks
  Threads within a block cooperate via shared memory and barrier synchronization
  Thread block scheduled on a single SM
  Consecutive k(=32) threads (within a block) form a warp
  Instrn. from a ready Warp is scheduled each cycle
…
float x =input[threadID];
float y = func(x);
output[threadID] = y;
…
threadID
Thread Block 0
…
…
float x =input[threadID];
float y = func(x);
output[threadID] = y;
…
Thread Block 1
…
float x =input[threadID];
float y = func(x);
output[threadID] = y;
…
Thread Block N - 1
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 32: Thread Batching: Grids and Blocks
Program consists of many kernels
A kernel is a grid of 1-D or 2-D thread blocks
Each thread block is a 1-D, 2-D or 3-D array of threads
All threads do the same work; programmer specifies what a thread does
Threads in a threadblock can cooperate with each other
  Synchronizing their execution
  Sharing data through a low latency shared memory
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Source : “NVIDIA CUDA Programming Guide”

## Slide 33: CUDA Programming
0
1
63
0
255

## Slide 34: CUDA Programming
cudaMalloc((void **) &d_x, size);
cudaMalloc((void **) &d_y, size);
cudaMemcpy(d_x, h_x, size, cudaMemcpyHostToDevice);
cudaMemcpy(d_y, h_y, size, cudaMemcpyHostToDevice);
saxpy_parallel <<<nblocks, 256>>>(n,2.0, d_x, d_y)
cudaMemcpy(h_y, d_y, size, cudaMemcpyDeviceToHost);
cudaFree(d_x); cudaFree(d_y);

## Slide 35: Accelerator – Fermi S2050

## Slide 36: Streaming Multiprocessor

## Slide 37: Inside a CUDA Core

## Slide 38: Memory Hierarchy in CUDA

## Slide 39: Global Memory

## Slide 40: Global Memory Accesses
Each thread issues memory accesses to data types of varying sizes, perhaps as small as 1 byte entities
Given an address to load or store, memory returns/updates “segments” of either 32 bytes, 64 bytes or 128 bytes
Maximizing bandwidth:
  Operate on an entire 128 byte segment for each memory transfer

## Slide 41: Understanding Global Memory Accesses
Memory protocol for compute capability 1.2 and 1.3* (CUDA Manual 5.1.2.1 and Appendix A.1)
Start with memory request by smallest numbered thread. Find the memory segment that contains the address (32, 64 or 128 byte segment, depending on data type)
Find other active threads requesting addresses within that segment and coalesce
Reduce transaction size if possible
Access memory and mark threads as “inactive”
Repeat until all threads in half-warp are serviced
*Includes Tesla and GTX platforms as well as new Linux machines!

## Slide 42: GPU cache hierarchy
GPU
Interconnection Network
SM Cluster
SM
SM
L2 $
Partition
GDDR5/HBM
L2 $
Partition
GDDR5/HBM
L2 $
Partition
GDDR5/HBM
Off-chip DRAM
SM Cluster
SM
SM
SM Cluster
SM
SM
L1 $
Coalescer
L1 $
L1 $
L1 $
L1 $
L1 $
Shared L2
Source: Arkaprava Basu, CSA, IISc

## Slide 43: Cache Comparison of GPU & CPU
 | CPU | GPU
L1 data cache capacity | 32KB | 16 KB
Active threads sharing L1 D Cache | 2 (2-way SMT) | 2560
L1 dcache capacity / thread | 16KB | 6.4 bytes
Last level cache (LLC) capacity | 8MB | 1MB
Active threads sharing LLC | 8 | 81,920
LLC capacity / thread (4 cores) | 1MB | 9.6 bytes
Example comparison of CPU and GPU cache hierarchy
Primary purpose of GPU cache is to act as bandwidth filter
Source: Arkaprava Basu, CSA, IISc

## Slide 44: GPU’s on-board memory
Goal: High bandwidth  need to service memory needs of thousands of active threads
  Latency is far less of a concern
High frequency and many channels
Low frequency but wide bus
Typical b/w: ~500-600 GB/sec (compare that too top end CPU server 150GB/sec)
But capacity is limited. Typical GPU memory capacity 12-16 GB with max at 32GB.
Source: Arkaprava Basu, CSA, IISc

## Slide 45: GPU TLB hierarchy
GPU
Interconnection Network
SM Cluster
SM
SM
L2 $
Partition
GDDR5/HBM
L2 $
Partition
GDDR5/HBM
L2 $
Partition
GDDR5/HBM
Off-chip DRAM
SM Cluster
SM
SM
SM Cluster
SM
SM
L1 $
Coalescer
L1 $
L1 $
L1 $
L1 $
L1 $
Shared L2
L1 TLB
L1 TLB
L1 TLB
L1 TLB
L1 TLB
L1 TLB
L2 TLB

## Slide 46: Resident Thread Blocks
No. of threadblocks allocated to SM is limited by
  Max. Threadblocks
  Max. no. of threads
  Registers (Regs. per thread * Thrds per Block * # Blks)
    16K – 64 K registers per SM
  Shared Memory (Shared Memory per Block * # Blks)
    16K – 64KB shared memory/L1

## Slide 47: Threadblock Scheduling
Each TB allocated to an SM; Multiple TBs in a SM
Thread Blocks can execute in any order
Threads in a threadblock may need to cooperate
  Load/Store from memory together
  Share results (through shared memory)
  Synchronize with each other

## Slide 48: Thread & Warp Scheduling
Each Block is executed as 32-thread Warps
  An implementation decision, not part of the CUDA programming model
  Warps are scheduling units in SM
Warps of resident threadblocks are context switched to hide (long) latency
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 1 Warps
Block 2 Warps
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Streaming Multiprocessor
Shared Memory
…
t0 t1 t2 … t31
…
Block 1 Warps
48
L2: Hardware Overview

## Slide 49: Warp Scheduling
Each SM launches Warps of Threads
  Shared instruction fetch per 32 threads (warps)
SM hardware implements zero-overhead Warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution on a prioritized scheduling policy
  All threads in a Warp execute the same instruction when selected
warp 8 instruction 11
SM multithreaded
Warp scheduler
warp 1 instruction 42
warp 3 instruction 95
warp 8 instruction 12
. . .
time
warp 3 instruction 96
Source : “Kirk-Hwu Lecture Notes”

## Slide 50: Context Switching to hide Latency

## Slide 51: How is context switching so efficient?
Large register file (16K – 64 K registers per SM)
  Each thread assigned a “window” of physical registers
  Works if entire thread block’s registers do not exceed capacity (otherwise, compiler fails)
  May be able to schedule from multiple blocks simultaneously
Similarly, shared memory requirements must not exceed capacity for all blocks simultaneously scheduled
Block 8
Thread 0
Block 0
Thread 0
Register File
Block 0
Thread 1
Block 0
Thread 256
Block 8
Thread 1
Block 8
Thread 256

## Slide 52: Warp Scheduling
Many different warp schedulers
  Loose Round Robin (LRR)
  Two level
  GTO
  Criticality-aware, cache-aware, progress-aware, …

## Slide 53: Kernel Execution

## Slide 54: Execution Model Comparison
MIMD/SPMD
SIMD/Vector
SIMT
Example Architecture | Multicore CPUs | x86 SSE/AVX | GPUs
Pros | More general: supports TLP | Can mix sequential & parallel code | Easier to program Gather/Scatter operations
Cons | Inefficient for data parallelism | Gather/Scatter can be awkward | Divergence kills performance
Source: Arkaprava Basu, CSA, IISc
Notes: Will explain pros/cons in depth later…this is a preview. End slide with: “Calling GPUs SIMT is a simplification. There is more to the story…”

## Slide 55: Branch Divergence Problem
GPU uses SIMD pipeline to save area on control logic.
  Group scalar threads into warps
Branch divergence occurs when threads inside warps branches to different execution paths.
Branch
Path A
Path B
Branch
Path A
Path B
Performance loss with SIMD width < 32

## Slide 56: PDOM-Based Reconvergence
-
G
1111
TOS
B
C
D
E
A
G
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B/1111
C/1001
D/0110
E/1111
A/1111
G/1111
-
A
1111
TOS
E
D
0110
E
C
1001
TOS
-
E
1111
E
D
0110
TOS
-
E
1111
A
D
G
A
Time
C
B
E
-
B
1111
TOS
-
E
1111
TOS
Reconv. PC
Next PC
Active Mask
Stack
E
D
0110
E
E
1001
TOS
-
E
1111

## Slide 57: Recent research in GPU
Integrated Heterogeneous Architectures / Heterogeneous System Architecture (HSA)
  CPU cores and GPU cores together in the same die
  Sharing of resources (including last level cache, memory, …)
Virtual memory support
  TLB /Address Translation for GPUs
  Supporting large pages in GPU
  Concurrent applicaions in GPU

## Slide 58: Recent research in GPU
Unified Address Space
  Unified Virtual Addressing (allocated at host, 32B transfers)
  Unified Memory (allocated at device, 4KB transfers)
  Unified Virtual Memory (UVM)