## Slide 1: Course Outline
  Processor Architecture, Caches, Instruction-Level Parallelism, Superscalar & VLIW architecture
  Multithreading, Multi-core processors, Cache Coherence and Memory Consistency; Multi-core Cache Organization
  Virtual Memory System
  Memory, DRAM Architecture
  Performance Evaluation
  Data-level Parallelism and Accelerators
  Power management
  Datacenter architecture
  Architecture Support for System Security

## Slide 2: Grading
1 Mid-Term Test = 20 marks
3 Assignment = 3x10 marks
  1 Programming exercise
  2 Written assignments (problem solving/term paper)
1 Term Project = 20 marks [Group of 2]
1 Final Exam = 30 marks
Text: Hennessy and Patterson, “Computer Architecture: A Quantitative Approach”:
  6th Ed. (Available in Indian Edition!)
  A large part of it would be assumed as reading exercise!

## Slide 3: Moore’s Law
No. of Transistors doubles every 18 months

## Slide 4: Moore’s Law : Other Implications

## Slide 5: Amdahl’s Law
  Speedup is limited by the part of the program which doesn’t benefit by an enhancement
Sp = = , for large k
1
s + (1-s)/k
1
s
  Example 1 : s = 0.5, k = 100, Sp = 1.81
  Maximum Speedup is 2!
  Example 2: s = 0.1, k = 10, Sp = 5.26.
  Moral : Make the common case faster!

## Slide 6: Pipelining : Review
IF
WB
MEM
EX
ID
IF
WB
MEM
EX
ID
IF
WB
MEM
EX
ID
IF
WB
MEM
EX
ID
Exec. Time of instrn. still 5 cycles, but throughput, now is 1 instrn. per cycle.
Initial pipeline fill time (4 cycles), after which 1 instrn. completes every cycle
Time
0
1
2
3
4
5
i
i +1
i +2
i +3
Instrn.

## Slide 7: Pipelined Processor Datapath
Ins.
Mem.
+
PC
Reg.
File
sign
extend
Instrn. Fetch
Instrn. Decode
4
ALU
Zero?
Data
Mem.
Execution
Memory
WB
IF/ID
ID/EX
EX/MEM
MEM/WB

## Slide 8: Pipeline Hazards
Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: Happen due to simultaneous request for the same resource by 2 or more instrns. (e.g., IF and MEM both require memory port!)
  Data hazards: Instruction depends on result of prior instruction still in the pipeline.
  Control hazards: Due to branch and jump instrns. Next PC (target PC) available only after 3 cycles (in EX stage) while IF has to take place in the next cycle!

## Slide 9: Structural Hazard
B
B
B
B
MEM and IF req. memory port
IF
WB
MEM
EX
ID
ld R3, 8(R2)
i
IF
WB
MEM
EX
ID
i + 1
IF
WB
MEM
EX
ID
i + 2
IF
i + 3
IF
WB
MEM
EX
ID
i + 3
B
Assume a single memory port

## Slide 10: Data Dependence
True data dependency (RAW)
Anti dependency -- write-after-read (WAR)
Output dependency -- write-after-write (WAW)
Example:
r3 <-- r7
r8 <-- load (r3)
r3 <-- r3 + 4
RAW
WAR
WAW

## Slide 11: Data Hazard
IF
WB
MEM
EX
ID
add R3  R1, R2
i
IF
WB
MEM
EX
ID
i + 1
sub R4  R3, R8
B
B
B
B
i + 1
WB
MEM
EX
ID
i + 1
WB
MEM
EX
ID
B
B
B
B
Time
0
1
2
3
4
5

## Slide 12: Data Hazard Solutions
Interlock: Hardware detect data dependency and stalls dependent instrns.
Byepassing or Forwarding: Computed data forwarded as soon as available (from EX or MEM stage)

## Slide 13: Data Hazard Solutions (contd.)
Forwarding or Bypassing : forward the result as soon as available (EX or MEM stage) to EX.
add R3  R1, R2
IF
WB
MEM
EX
ID
or R7  R3, R6
IF
EX
ID
sub R5  R3, R4
IF
MEM
EX
ID

## Slide 14: Processor Datapath for Forwarding
Imm
NPC
ALU
Zero?
Data
Mem.
Execution
Memory
B
A

## Slide 15: Data Hazard Solutions
Interlock: Hardware detect data dependency and stalls dependent instrns.
Byepassing or Forwarding: Computed data forwarded as soon as available (from EX or MEM stage)
  For what Ops from MEM stage?
  Can byepassing avoid all stalls?

## Slide 16: Forwarding may not always Work!
ld R3  M(R1)
IF
WB
MEM
EX
ID
or R7  R3, R6
IF
EX
ID
sub R5  R3, R4
IF
MEM
EX
ID
  Forwarding cannot eliminate all stalls in deep pipelines!

## Slide 17: Data Hazard Solutions
Interlock: Hardware detect data dependency and stalls dependent instrns.
Byepassing or Forwarding: Computed data forwarded as soon as available (from EX or MEM stage)
  For what Ops from MEM stage?
  Can byepassing avoid all stalls?
Instruction Scheduling: Reorder instrns. such that dependent instrns. are 2-3 cycles apart.
  Static Instruction Scheduling
  Dynamic Instruction Scheduling

## Slide 18: Control Hazard
Fetch instrn. (i +1) or from target?
IF
MEM
EX
ID
B
B
B
B
B
IF
EX
ID
Fetch instrn. (i +1) or from target?
IF
ID
Branch resolved Fetch appropriate instrn.
beqz R3, out
IF
WB
MEM
EX
ID
Cond. & target resolved here
B
B
B
B

## Slide 19: Pipelined MIPS Datapath
Ins.
Mem.
+
PC
Reg.
File
sign
extend
Instrn. Fetch
Instrn. Decode
4
ALU
Data
Mem.
Execution
Memory
WB
IF/ID
ID/EX
EX/MEM
MEM/WB
Zero?
Adder

## Slide 20: Control Hazard Solutions
    nop
Static Branch prediction policies:
  Static Not-Taken policy:
  Fetch instrn. from PC + 4 even for a branch instrn.
    Squash the fetched instrn, and re-fetch from branch target address
  Delayed Branching:
  microarchitecture designed such that branch (control transfer) takes place after a few following instructions.
(delay slot instrn.)
    add R3 <-- R2, R4
    beq R1, out
    add R3 <-- R2, R4

## Slide 21: Delayed Branching
Instrns. that do not affect the branching condition can be used in the delay slot.
Where to get instrns. for filling delay slots?
  Instrns. Before the branch
  Instrns. from the target address
  Instrns. from fall through
Cancelling delayed branches, which squash the instrn. in the delayed when the branch is taken (or not taken) -- facilitate more slots to be filled.

## Slide 22: Dynamic Branch Prediction
For the same static branch instrn. prediction for different instances may be different.
Using the history of branches to predict the branch outcome (taken or not-taken)
  1-bit predictors
  2-bit predictors
  2-level correlated predictors
  path-based predictors, …

## Slide 23: Simple 1-bit Branch Prediction
Store previous history of a branch -- taken or not-taken (1-bit) in Branch Prediction Buffer
Least Significant bits of PC used to index BPB.
Update Predict bit after branch is resolved.
Predict branch outcome only, not target address.
Influence of other (static) branches which have same LS bits (alias)
PC
BPB (2048 entries)
0
0  Not taken
1  Taken
1-bit prediction will mispredict twice on every loop.

## Slide 24: 2-bit Branch Prediction
State of each static branch represented by 2-bits.
Implement the State machine
Different state transition diagram for diff. 2-bit schemes.
Implementation using saturating counters ?
Gives high prediction accuracy 85% to 95%.
Taken
0
ST
WT
WNT
SNT
Not-Taken
Taken
Taken
Taken
Not-Taken
Not-Taken
Not-Taken

## Slide 25: 2-bit Prediction
Still no prediction of target address!
With a 2-bit prediction the no. of mispredictions of branch b1 is lower!
L1: R2  100
…
L2: R1,  100
…
R1  R1 - 1
b1: bne R1, L2
R2  R2 - 1
b2: bne R2, L1
PC
BPB (2048 entries)
10
00, 01  Not taken
10, 11  Taken
What is the benefit of 2-bit over 1-bit?

## Slide 26: Branch Target Buffer
Store branch target address (computed when the static branch instrn. is encountered first) along with prediction bits -- Branch Target Buffer.
Associate tag bits to avoid other (branch) instrns. influence the prediction.
When to make the prediction?
  Prediction can be made in IF stage itself! no stall on correct prediction.
Size of BTB = 2048x52 !
=
00
PC
Target Addr.
Tag
No: Don’t Predict
Yes: Predict
V

## Slide 27: Other Branch Prediction Schemes
A
D
E
F
B
C
E
F
G
D
B
C
A
Correlated Prediction
Path Prediction
D is taken if A is not taken

## Slide 28: 2-Level Branch Prediction
2-bit scheme uses the history of the same static branch for prediction.
In practice, history of other branches also influence branching.
history | br1 | 1 | 1 | 0 | 0
 | br2 | 1 | 0 | 1 | 0
Pred. | br3 | 1 | 1 | 1 | ?
  if (aa == 2) aa = 0;
  if (bb != 2) bb = 0;
  if (aa == 0) || (bb == 0) { …

## Slide 29: 2-Level Prediction (contd.)
Branch history register/table to maintain the outcome of previous (dynamic) k branches.
Pattern History table(s) to record the branch behavior (2-bit FSM).
Branch history can be global or local
Pattern history can be global or local.
Other variations (g-share, p-share)
Results upto 98% prediction accuracy.
Reading:
  TseYu Yeh and Yale N Patt, “Alternative Implementations of TwoLevel Adaptive Branch Prediction”, ISCA 92

## Slide 30: GAg and GAp Schemes
BHR (k-bit)
Pred.
PHT (2k entries)
0/1
Global branch history register & global pattern history table
BHR (k-bit)
Pred.
PPHT (2k x 2m)
PC
Global branch history reg. and per addr. pattern history table

## Slide 31: PAp Scheme
PPHT (2k x 2n)
PC
PBHT (2m k-bit entries)
n-bits
m-bits

## Slide 32: Comparison of 2-Level Schemes
In GAg, 1st-level history is based on last k dynamic branches.
No per-addr. Branch or pattern history.
History of all branches influence prediction.
In GAp, correlation of other branches, and past behavior of this branch influence prediction.
In PAg, per-addr. branch history is maintained.
History of a branch influence its prediction; but same pattern behavior for all branches
PAp other branches influence is least.
Per-Set schemes use addr., opcode type, etc. to determine sets.

## Slide 33: G-Share and Other Predictors
G-share is similar to GAg, except that BHR is XORed with PC to index in PHT.
  Eliminates interference of same branch history across different branches.
2-Level predictors have longer warm-up time to build history. Frequent context-switching affects building the history.
Hybrid predictors take advantage of multiple predictors.
Path-based schemes using history of target addresses of branches and not their outcomes.

## Slide 34: Hybrid Predictors
Global predictor: Has 4K entries and is indexed by the history of the last 12 branches; each entry in the global predictor is a standard 2-bit predictor
Local predictor: Consists of a 2-level predictor:
  Top level a local history table consisting of 1024 10-bit entries; each 10-bit entry corresponds to the most recent 10 branch outcomes for the entry.
  Next level Selected entry from the local history table is used to index a table of 1K entries consisting a 3-bit saturating counters, which provide the local prediction
4K 2-bit counters to choose between the global predictor and local predictor
Total size: 4K*2 + 4K*2 + 1K*10 + 1K*3 = 29K bits!
(~180,000 transistors)

## Slide 35: Tournament Predictor in 21264
Pred.
BHR
2
GlobalPred.
Meta Pred.
PC
3
Local Pred.
PBHT
PHT

## Slide 36: Indirect Branches
Branches or jumps whose target addr. varies at runtime.
  Function return, jumps for implementing case statements, etc.
  Target address prediction for function returns using a return address stack of size 8 to 16.