## Slide 1
Samira Khan
University of Virginia
April 26, 2016
COMPUTER ARCHITECTURE
CS 6354
Prefetching
The content and concept of this course are adapted from CMU ECE 740
Adapted from Samira Khan, University of Virginia

## Slide 2: Prefetching
Idea: Fetch the data before it is needed (i.e. pre-fetch) by the program
Why?
  Memory latency is high. If we can prefetch accurately and early enough we can reduce/eliminate that latency.
  Can eliminate compulsory cache misses
  Can it eliminate all cache misses? Capacity, conflict?
Involves predicting which address will be needed in the future
  Works if programs have predictable miss address patterns

## Slide 3: Basics
In modern systems, prefetching is usually done in cache block granularity
Prefetching is a technique that can reduce both
  Miss rate
  Miss latency
Prefetching can be done by
  hardware
  compiler
  programmer

## Slide 4: How a HW Prefetcher Fits in the Memory System

## Slide 5: Prefetching: The Four Questions
What
  What addresses to prefetch
When
  When to initiate a prefetch request
Where
  Where to place the prefetched data
How
  Software, hardware, execution-based, cooperative

## Slide 6: Challenges in Prefetching: What
What addresses to prefetch
  Prefetching useless data wastes resources
    Memory bandwidth
    Cache or prefetch buffer space
    Energy consumption
  Accurate prediction of addresses to prefetch is important
    Prefetch accuracy = used prefetches / sent prefetches
How do we know what to prefetch
  Predict based on past access patterns
  Use the compiler’s knowledge of data structures
Prefetching algorithm determines what to prefetch

## Slide 7: Challenges in Prefetching: When
When to initiate a prefetch request
  Prefetching too early
    Prefetched data may be evicted before use
  Prefetching too late
    Might not hide the whole memory latency
When a data item is prefetched affects the timeliness of the prefetcher
Prefetcher can be made more timely by
  Making it more aggressive: try to stay far ahead of the processor’s access stream (hardware)
  Moving the prefetch instructions earlier in the code (software)

## Slide 8: Challenges in Prefetching: Where (I)
Where to place the prefetched data
  In cache
    + Simple design, no need for separate buffers
    -- Can evict useful demand data  cache pollution
  In a separate prefetch buffer
    + Demand data protected from prefetches  no cache pollution
    -- More complex memory system design
    - Where to place and how to size the prefetch buffer
    - When to access the prefetch buffer (parallel vs. serial with cache)
    - When to move the data from the prefetch buffer to cache
Many modern systems place prefetched data in the cache
  Intel Pentium 4, Core2’s, AMD systems, IBM POWER4,5,6,

## Slide 9: Challenges in Prefetching: Where (II)
Where to place the prefetched data in the cache?
  Do we treat prefetched blocks the same as demand-fetched blocks?
  Prefetched blocks are not known to be needed
    With LRU, a demand block is placed into the MRU position
Do we skew the replacement policy such that it favors the demand-fetched blocks?
  E.g., place all prefetches into the LRU position in a way?
Which level of cache to prefetch into?
  Memory to L2, memory to L1. Advantages/disadvantages?
  L2 to L1? (a separate prefetcher between levels)

## Slide 10: Prefetcher Performance
Prefetch Accuracy
  Ratio of prefetch hits to number of prefetches
  Higher accuracy => better performance, less wasted resources!
Prefetch Coverage
  Fraction of original misses eliminated by prefetched lines; that is ratio of prefetch hits to number of misses (without prefetching)
  Higher coverage is important for prefetchto be effective
Timeliness
  A prefetch is timely is the prefetch request is completed and the data are placed in cache, and not evicted by other requests
  Ratio of on-time prefetches / useful prefetches

## Slide 11: Prefetcher Parameters
For most hardware prefetchers:
  Prefetch distance: how far ahead of the demand stream
  Prefetch degree: how many prefetches per demand access
Prefetch
Distance
Predicted Stream
X
Access Stream
(X+P)
Prefetch Degree
X+1
1 2 3

## Slide 12: Challenges in Prefetching: How
Software prefetching
  ISA provides prefetch instructions
  Programmer or compiler inserts prefetch instructions (effort)
  Usually works well only for “regular access patterns”
Hardware prefetching
  Hardware monitors processor accesses
  Memorizes or finds patterns/strides
  Generates prefetch addresses automatically
Execution-based prefetchers
  A “thread” is executed to prefetch data for the main program
  Can be generated by either software/programmer or hardware

## Slide 13: Software Prefetching
Idea: Compiler/programmer places prefetch instructions into appropriate places in code
  Mowry et al., “Design and Evaluation of a Compiler Algorithm for Prefetching,” ASPLOS 1992.
Prefetch instructions prefetch data into caches
Compiler or programmer can insert such instructions into the program

## Slide 14: Software Prefetching (II)
Can work for very regular array-based access patterns. Issues:
  -- Prefetch instructions take up processing/execution bandwidth
  How early to prefetch? Determining this is difficult
    -- Prefetch distance depends on hardware implementation (memory latency, cache size, time between loop iterations)  portability?
    -- Going too far back in code reduces accuracy (branches in between)
  Need “special” prefetch instructions in ISA?
    Alpha load into register 31 treated as prefetch (r31==0)
    PowerPC dcbt (data cache block touch) instruction
  -- Not easy to do for pointer-based data structures
for (i=0; i<N; i++) {
__prefetch(a[i+8]);
__prefetch(b[i+8]);
sum += a[i]*b[i];
}
while (p) {
__prefetch(pnext);
work(pdata);
p = pnext;
}
while (p) {
__prefetch(pnextnextnext);
work(pdata);
p = pnext;
}
Which one is better?

## Slide 15: Hardware Prefetching
Idea: Specialized hardware observes load/store access patterns and prefetches data based on past access behavior
Tradeoffs:
  + Can be tuned to system implementation
  + Does not waste instruction execution bandwidth
  -- More hardware complexity to detect patterns

## Slide 16: Next-Line Prefetchers
Simplest form of hardware prefetching: always prefetch next N cache lines after a demand access (or a demand miss)
  Next-line prefetcher (or next sequential prefetcher)
  Tradeoffs:
    + Simple to implement. No need for sophisticated pattern detection
    + Works well for sequential/streaming access patterns
    -- Inaccurate with irregular patterns and wastes bandwidth
    -- And, even regular patterns:
    - What is the prefetch accuracy if access stride = 2 and N = 1?
    - What if the program is traversing memory from higher to lower addresses?
    - Also prefetch “previous” N cache lines?

## Slide 17: Stride Prefetchers
Two kinds
  Instruction program counter (PC) based
  Cache block address based
Instruction based:
  Baer and Chen, “An effective on-chip preloading scheme to reduce data access penalty,” SC 1991.
  Idea:
    Record the distance between the memory addresses referenced by a load instruction (i.e. stride of the load) as well as the last address referenced by the load
    Next time the same load instruction is fetched, prefetch last address + stride

## Slide 18: Instruction Based Stride Prefetching
  Late prefetches
    Prefetch ahead (last address + N*stride)
    Generate multiple prefetches
  How far can the prefetcher get ahead of demand accesses? Use lookahead PC to index the prefetcher table
Load Inst. Tag | Last Address | Last Stride | Confidence
……. | ……. | …… | ……
Effective Addr.
Load PC
+
-
Prefetch
Address

## Slide 19: Cache Address Based Stride Prefetching
Can detect
  A, A+N, A+2N, A+3N, …
  Stream buffers are a special case of cache block address based stride prefetching where N = 1
Last Address | Last Stride | Confidence
……. | …… | ……
Effective Addr.
+
-
Prefetch
Address

## Slide 20: Stream Buffers (Jouppi, ISCA 1990)
Each stream buffer holds one stream of sequentially prefetched cache lines
On a load miss check the head of all stream buffers for an address match
  if hit, pop the entry from FIFO, update the cache with data
  if not, allocate a new stream buffer to the new miss address (may have to recycle a stream buffer following LRU policy)
Stream buffer FIFOs are continuously topped-off with subsequent cache lines whenever there is room and the bus is not busy
FIFO
FIFO
FIFO
FIFO
DCache
Memory interface
Jouppi, “Improving Direct-Mapped Cache Performance by the Addition of a Small Fully-Associative Cache and Prefetch Buffers,” ISCA 1990.

## Slide 21: Stream Buffer Design

## Slide 22: Prefetching Using a Global History Buffer
Kyle J. Nesbit and James E. Smith
Adapted from K.J.Nesbit’s Talk

## Slide 23: Markov Prefetching
Markov prefetching forms address correlations
  Joseph and Grunwald (ISCA ‘97)
Uses global memory addresses as states in the Markov graph
Correlation Table approximates Markov graph
A B C A B C B C . . .
Miss Address Stream
A
B
C
1
.5
1
.5
Markov Graph
B
C
B
A
B
C
Correlation Table
1st predict.
2nd predict.
miss
address
A

## Slide 24: Correlation Prefetching
Distance Prefetching forms delta correlations
  Kandiraju and Sivasubramaniam (ISCA ‘02)
Delta-based prefetching leads to much smaller table than “classical” Markov Prefetching
Delta-based prefetching can remove compulsory misses
Markov Prefetching
1 1 -2 1 1 -1 1
Global Delta Stream
Distance Prefetching
27 28 29 27 28 29 28 29
Miss Address Stream
28
29
28
29
27
28
29
1st predict.
2nd predict.
miss
address
1
1
-1
-2
-2
-1
1
global
delta
1st predict.
2nd predict.
Notes: Fixme: update correlation table – make fonts larger in example

## Slide 25: Prefetching using Global History Buffer (GHB): Motivation
Table-based prefetch predictors are inefficient
  Reserve fixed amount of space per prefetch key
  Stale entries in the table corpg. to old history  lead to ineffective prefetch!
Unifying structure for seemingly different predictors
  PC-based constant stride
  Markov Prefetch
  Distance (Delta) Prefetch

## Slide 26: Global History Buffer (GHB)
Holds miss address history in FIFO order
Linked lists within GHB connect related addresses
  Same static load
  Same global miss address
  Same global delta
Global History Buffer
miss addresses
FI
Index Table
Load PC
FO
Index Table
  Accessed with a key
  Load PC, Miss address, or Delta’s
  Used for Localization/Otherwise

## Slide 27: GHB – Example (Markov Prefetching)
Miss Address Stream
Global History Buffer
miss address
pointer
pointer
Index Table
28
29
29
29
head pointer
28
27
27
27 28 29 27 28 29 28
27
=> Current
=> Prefetches
Key
28
29
28
29
Global Miss
Address
Notes: Change addresses to be consistent – make numbers larger, darker

## Slide 28: Prefetch Taxonomy
To simplify the discussion and illustrate the relation between prefetching methods we introduce a consistent naming convention.
Each name is a X/Y pair.
  X is the key used for localizing the address stream.
  Y is the method for detecting address patterns.

## Slide 29: Prefetch Taxonomy
We study two localizing methods
  Program Counter (PC)
  No localization or global (G)
And three pattern detection methods
  Address Correlation
  Delta Correlation
  Constant Stride

## Slide 30: Existing Prefetch Methods in Prefetch Taxonomy
Markov Prefetching - G/AC
Distance Prefetching - G/DC
Stride Prefetching - PC/CS

## Slide 31: GHB – Example (PC-based Stride Prefetching)
Miss Address Stream for PC2: A, A+s, A+2s, …
Global Miss Address Stream: A, (C-j), A+s, (B-k), B, (C-i), C, A+2s, …
Global History Buffer
miss address
pointer
pointer
Index Table
PC2
PC3
head pointer
PC1
A+2s
Load PC
A+s
A
B
C
Notes: Change addresses to be consistent – make numbers larger, darker

## Slide 32: Prefetching: Width, Depth, and Hybrid
1
4
8
1 8 8 1 4 4 1 8 8
Global Delta Stream
Miss Address Stream
27 28 36 44 45 49 53 54 62 70
71
1
1
8
=> Current
=> Prefetches
Key
8
4
4
Width
Depth
Hybrid
Markov Graph
.3
.3
.3
.7
.7
.7
71 + 8 => 79
79 + 8 => 87
Prefetches
71 + 4 => 75
79 + 4 => 79
Prefetches
71 + 8 => 79
71 + 4 => 75
Prefetches
Notes: Add absolute prefetch addresses

## Slide 33: GHB – Hybrid Delta
Width prefetching suffers from poor accuracy and short look-ahead
Depth prefetching has good look-ahead, but may miss prefetch opportunities when a number of “next” addresses have similar probability
The hybrid method combines depth and width

## Slide 34: GHB - Hybrid Example
79 + 4 => 79
71 + 4 => 75
Global History Buffer
miss address
pointer
pointer
Index Table
head pointer
27
28
36
44
45
49
53
1
1
=> Current
=> Prefetches
Key
54
62
70
4
8
8
8
Global
Delta
1 8 8 1 4 4 1 8 8
Global Delta Stream
Miss Address Stream
27 28 36 44 45 49 53 54 62 70
71
1
8
4
4
71
8
71 + 8 => 79
79 + 8 => 87
Prefetches

## Slide 35: Simulation Methodology
Simulated SPEC CPU2000 benchmarks
Fast forwarded 1 billion instructions and simulated 1 billion instructions
Used peak binaries compiled -O4 optimization
Results include all benchmarks that have at least a 5% IPC improvement with an ideal L2 cache
Issue Width | 4 Instructions
Load Store Queue | 64 Entries
RUU Size | 128 Entries
Level 1 D-Cache | 16 KB, 2-way
Level 1 I-Cache | 16 KB, 2-way
Level 2 Cache | 512 KB, 4-way
Memory Latency | 140 Cycles

## Slide 36: Simulation Methodology
Table walk - one cycle per access
IT size reduces table conflicts
GHB size reflects prefetch history working set
In general, the GHB prefetching requires less history
Prefetching Method | Table Configuration | Size
Conventional Distance Prefetching | 512 Table Entries | 18 KB
GHB Distance Prefetching | 512 IT Entries & 512 GHB Entries | 8 KB

## Slide 37
Distance Prefetching (Performance)
5%
15%
25%
35%
1
2
4
8
16
Prefetch Degree
Table (width)
GHB (width)
GHB (depth)
GHB (hybrid)
IPC Improvement

## Slide 38
Distance Prefetching (Performance)
-10%
10%
30%
50%
70%
90%
110%
ammp
art
wupwise
swim
lucas
mgrid
applu
galgel
apsi
mcf
twolf
vpr
parser
gap
bzip2
hmean
Table (width)
GHB (width)
GHB (depth)
GHB (hybrid)
IPC Improvement
(~300%)

## Slide 39
Distance Prefetching (Memory Traffic)
0%
30%
60%
90%
120%
150%
180%
1
2
4
8
16
Prefetch Degree
Table (width)
GHB (width)
GHB (depth)
GHB (hybrid)
Increase in Memory Traffic

## Slide 41: Content Directed Prefetching (I)
A specialized prefetcher for pointer values
Cooksey et al., “A stateless, content-directed data prefetching mechanism,” ASPLOS 2002.
Idea: Identify pointers among all values in a fetched cache block and issue prefetch requests for them.
+ No need to memorize/record past addresses!
+ Can eliminate compulsory misses (never-seen pointers)
-- Indiscriminately prefetches all pointers in a cache block
How to identify pointer addresses:
  Compare address sized values within cache block with cache block’s address  if most-significant few bits match, pointer
Source: Onur Mutlu, CMU, ECE-740, Fall-2011

## Slide 42: Content Directed Prefetching (II)
x40373551
L2
DRAM
…
…
=
=
=
=
=
=
=
=
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
x80011100
Generate Prefetch
Virtual Address Predictor
X80022220
22220
X800
11100
x800
Source: Onur Mutlu, CMU, ECE-740, Fall-2011

## Slide 43: Other Prefetching Methods
Somogyi et al., “Spatio-Temporal Memory Streaming,” ISCA 2007.
Idea: Combining spatial and temporal prefetch predictors.
  Temporal Predictor: Recurring memory access sequences
  Spatial Predictor: Recurring data layouts (structs)
Ishii et al., “Access Map Pattern Matching” Jl. of ILP, 2011
  Idea: Captures simple repeating access patterns through an array of 2 bit values.
Shevgoor, et al., “Variable Length Delta Prefetcher”, Micro 2015
  Idea: Learns multiple delta sequences from variable length Delta History Buffer (per page)
Data Prefetch Championship, held along with ISCA