## Slide 1: VI Snooping Protocol (for write-back/write-allocate)
1 bit to tack coherence state per cache block
  Valid/Invalid
Default state of any address not present in cache is “Invalid”
Processor Actions
  Ld, St, Evict
Bus Messages
  BusRd, BusWr
Store / BusWr
BusWr / --
Store / BusWr
Load / BusRd
Load / --
Valid
Invalid
Evict / BusWB
Transition caused by local action
Transition caused by bus message
Notes: 9